## Slide 1: Improving the Current Loop Bandwidth and Axis Decoupling for High Speed Electrical Drives Using Multisampled Control

## Slide 2
01
04
02
Table of Contents
03
INTRODUCTION
Goal & motivation
Limitations
IMPLEMENTATION
DSP algorithm
Timings & averaging
CURRENT PROGRESS
Simulink
HIL
Analytics
FUTURE PLAN

## Slide 3
01
04
02
Table of Contents
03
INTRODUCTION
Goal & motivation
Limitations
IMPLEMENTATION
DSP algorithm
Timings & averaging
CURRENT PROGRESS
Simulink
HIL
Analytics
FUTURE PLAN

## Slide 4
Multisampling control - basics
(k-1)Tsw
kTsw
(k+1)Tsw
t
iL(t)
iL,f [k]
(k-1)Tsw
kTsw
(k+1)Tsw
t
iL(t)
iL,f [k]
Single Sampling Approach
fsampling = fsw
Multiple Sampling Approach
fsampling = N·fsw

## Slide 5
Multisampling - motivation
Digital delays are reduced!
Combined DPWM and one-step computational delay is equal to:

## Slide 6
Multisampling - problems
Vertical crossings between modulating waveform and carrier introduce DPWM nonlinearity
  Transcharacterisctics (D = f(<m>)) shows reduced gain regions [1]:
      Gain = ½ for one edge vertical crossing
      Gain = 0 for two edge vertical crossings
These are solved by using ripple filtering:
  Repetitive filters [2]
    less phase-lag
    sensitive to noise
  One-period averaging (MAFs)
    better noise performance
In DSPs additional “trick” is needed as switching occurs when compare register is equal to the carrier (pulse skipping would occur at vertical crossings if this algorithm would not be implemented)
[1]: Corradini, L. and Mattavelli, P., 2008. Modeling of multisampled pulse width modulators for digitally controlled DC–DC converters. IEEE Transactions on Power Electronics, 23(4), pp.1839-1847.
[2]: Corradini, L., Mattavelli, P., Tedeschi, E. and Trevisan, D., 2008. High-bandwidth multisampled digitally controlled DC–DC converters using ripple compensation. IEEE Transactions on Industrial Electronics, 55(4), pp.1501-1508.

## Slide 7: Bonus: Multisampling DSP algorithm
Example: UR=4
No missed edges due to vertical crossings
Only one ePWM module that runs on control frequency (UR*fpwm)
The maximum and minimum values of the virtual carrier, for the following control period are used to distinct cases with horizontal and vertical intersections with the virtual carrier

## Slide 8
01
04
02
Table of Contents
03
INTRODUCTION
Goal & motivation
Limitations
IMPLEMENTATION
DSP algorithm
Timings & averaging
Parameter design
CURRENT PROGRESS
Simulink
HIL
FUTURE PLAN

## Slide 9
DSP uses DMA for high-frequency sampling (the same as in [3]), with rate Nmaf = Tsw / Tdma
Every Ts = Tsw / N, results from DMA are gathered
  First they are averaged in alpha-beta frame over Ts
  Second, this value is transformed to DQ frame using average of angles during previous Ts
  Thirdly, these dq values are averaged in DQ frame over Tsw
The controller updates its output N times per Tsw
  The controller structure is obtained using ZOH model (the same as in [3])
  The gain alpha is chosen relative to new Ts (PWM frequency limits the bandwidth, not the sampling frequency)
Proposed algorithm structure
[3]: Vukosavić, S.N., Perić, L.S. and Levi, E., 2015. AC current controller with error-free feedback acquisition system. IEEE Transactions on Energy Conversion, 31(1), pp.381-391.
Example: N = 4, Nmaf = 16

## Slide 10
Timings & averaging
Feedback averaging
  Current: Moving Average Filter (MAF) over one switching period
  Angle: averaging on regulation period
fpwm=10kHz, Nmaf=16, UR<=8

## Slide 11
Regular double update (without one-period averaging)
Multisampled update with one-period averaging
Time delay comparison
Starting from N > 6, Multisampled update with simple one-period averaging brings dynamic improvements compared to N = 2.
  One-period averaging removes ripple -> no multisampling related nonlinearities are present
Derivative gain is potentially introduced to improve controller (as in [3]):
  Procedure for derivative gain tuning (at least for good initial guess):
  For one period averaging, this corresponds to adding a zero on
  Discretization of derivative action should also not be problematic below as sampling frequency is increased
One period averaging equivalent time delay
Control + DPWM equivalent time delay

## Slide 12
Benefits:
  Reduced time delay -> better stability margins
  Angle information is obtained multiple times per switching period
    Averaging in dq frame as well (not only in alpha-beta and then transformed to dq)
    Better decoupling capability
Demerits:
  The model in z-domain now doesn’t completely match the large-signal system dynamics, due to fs > 2*fpwm (not every controller output modifies the PWM output).
  Care should be taken in limiting the upper value of alpha, according to feasible bandwidths – limited by the fpwm.
Target for publication

## Slide 13
01
04
02
Table of Contents
03
INTRODUCTION
Goal & motivation
Limitations
IMPLEMENTATION
DSP algorithm
Timings & averaging
Parameter design
CURRENT PROGRESS
Simulink
HIL
FUTURE PLAN

## Slide 14
Current progress – Simulink (1)
BLDC parameters (vukosavic2016.pdf):
  Rs=0.47Ω, Ls=3.4mH, kemf=0.687 Vpeak/(rad/s), Inom=7.3A
Simulation step time is set acc. to EPWM clock (100MHz) in oroder to accuretely model DPWM block
IMC IREG (no diff. action):

## Slide 15: Current progress – Simulink (2)
DQ step response
  UR=8 VS. UR=2 (both with MAF 16x)
  For UR=8 α is set to obtain same overshoot as for UR=2 with alpha=0.2
Update rate (UR) | 2 | 8
MAF | yes | yes
α | 0.2 | 0.087
OS | 4.7% | 5%
T_rise(10% - 90 %) | 2.5 Tsw | 1.5 Tsw
Simulink: UR=2 with MAF, α=0.2
Simulink: UR=8 with MAF, α=0.087

## Slide 16
Current progress - HIL
Typhoon HIL 402 & F28379D launch pad
Similar parameter settings as in Simulink
Update rate (UR) | 2 | 8
MAF | yes | yes
α | 0.2 | 0.087
OS | 7% | 6.7%
T_rise(10% - 90 %) | 2.5 Tsw | 1.5 Tsw
Oscilations
@ fundamental
Oscilations
@ fundamental
HIL: UR=2 with MAF, α=0.2
HIL: UR=8 with MAF, α=0.087

## Slide 17: Current progress and encountered problems
Derivative gain is not yet finely tuned
  Goal is to obtain better results than N = 2 + derivative gain
Oscillations on fundamental frequency:
  Present also for N = 2 with averaging (so not related to multisampling)
Best way to point in the paper?
  Go for the same bandwidth as in [4] with higher stability margin?
  Test decoupling at very high speeds (RL load)?
HIL: UR=2 with MAF, α=0.2
HIL: UR=8 with MAF, α=0.087
[4]: Vukosavić, S.N., Perić, L.S. and Levi, E., 2016. A three-phase digital current controller with improved performance indices. IEEE Transactions on Energy Conversion, 32(1), pp.184-193.

## Slide 18
01
04
02
Table of Contents
03
INTRODUCTION
Goal & motivation
Limitations
IMPLEMENTATION
DSP algorithm
Timings & averaging
Parameter design
CURRENT PROGRESS
Simulink
HIL
FUTURE PLAN

## Slide 19
Future work
Idq oscillations
@ fundamental
Location of best validation “target” for publication
Experimental
validation

## Slide 20: Work plan and help needed
Experimental testing environment
  Ruzica can perform the tests
  TI f28379D (code is ready)
  MOOG inverter
Help needed to properly place the paper + all ideas / critiques are welcome
I talked about this with Paolo and Simone Buso, and they fully support if we want to collaborate (UniPD + ETF Bgd) as this is directly related to my PhD (my plan is to later also investigate multisampling benefits for passivity of grid-connected converters due to reduced delays).